UMass Lowell Blue Title Slide
University Of Massachusetts Lowell
STARK

---
UMass Lowell Blue Secondary
Chassis
- 4 wheel tank steering
- All aluminum chassis
- Detachable electronics case
- Detachable sensor mast

---
Power System
- Batteries
  - 2x 50Ah 12v SLA batteries in series
- Motor Power
  - Raw 24v
- Logic Power
  - 12v powered by 24-12v high efficiency Vicor DC-DC inverter.
  - M2ATX smart automotive PSU
- Sensor Power
  - SICK Lidar powered by 24-24v high efficiency Vicor DC-DC inverter.
  - GPS/Camera/Compass powered by computer

---
Safety System
- On board
  - Front and rear mounted kill switches
  - Easily reachable from all sides
- Wireless
  - 900mhz Xbee based
  - 1/4 mile range
  - Heartbeat
  - Feedback on remote

---
Sensors
- Obstacle Detection
  - SICK LMS Lidar
  - Sony Playstation-eye Camera
- Localization
  - USGlobalsat GPS
  - MediaTek GPS
  - Ocean Server 0S5000 Compass
  - US Digital E5 encoders (512 c/r)

---
ROS

---
Software Architecture

---
Vision
White Feature Detection
  - White Lines
  - Barrels
  - Saw horses
1. Birds Eye Projection
2. Laser Scan
  1. Ray casting to white pixels
  2. Generate Laser Scan
  3. Merge with laser map

---
Navigation

---
Cost
Component	Cost
Aluminum Frame	$1500
Motors	$700
Motor Controller	$350
Batteries	$200
Battery Charger	$250
Power Distribution System	$300
E-Stop System	$250
Computer System	$350
Camera	$50
Compass	$300
GPS	$150
Lidar	$5000
TOTAL	$9400

---
Thank You